## Slide 1: A Functional Modeling Framework for Composable System Analysis
July 18, 2022

## Slide 2: Motivation
Capture the ability of composable systems to satisfy non-trivial functional capabilities
Must not be restricted to arbitrary functional levels (e.g., capabilities, activities, functions), and must handle all relevant forms of constraint between systems and functions
Simplify the rules and modeling element types as much as possible while enabling modelers to capture the relevant phenomena with the least amount of effort

## Slide 3
Capabilities
Activities
Functions
System-of-Systems
Systems
Sub-systems
Validation
Verification
Collaborate as…
Integrated
Into…
Provided by
Require
Require
Functions
Systems

## Slide 4: What are Functions?
A function is any activity or purpose, they are something to be done
They must be clearly defined
They should not reference a system or class of system
Functions are represented as ovals, e.g.,
fA

## Slide 5: What are Systems?
Systems are represented as squares, e.g.,
S1
Systems are things that accomplish a function
They may be physical or non-physical
In this formulation systems cannot be mutated or parametrized, a system exists as is and cannot be modified

## Slide 6: Legend
fA
S1
A function called fA
A system called S1
A satisfies relationship
A requires relationship
An incompatible relationship
These are the only elements that can be used to describe systems in the framework

## Slide 7: Function Relationships
fA
fB
fC
function fA is satisfied by either function fB or fC
fA
fB
fC
function fA requires both function fB and fC
OR dependency
AND dependency
Notes: A function may be satisfied by other functions, e.g., to detect an airborne threat, the AAW officer could receive a warning from a warning receiver (if the aircraft is targeting the ship), detect it with an active radar, or receive information from another sensor through a datalink. This corresponds to a series of OR statements for satisfying a function, e.g., this function can be satisfied by this function OR this other function.
A function may require a series of functions to be satisfied, e.g., in order to successfully intercept an airborne threat, the ship must be able to find, fix, track, target, engage the threat and assess if the engagement was successful. Each one of those functions must be satisfied for the interception to be achieved. In this case the function is satisfied by a series of AND statements, e.g., in order to achieve this function, this function AND this other function have to be achieved.

## Slide 8: System Relationships
OR satisfaction
AND dependency
fA
function fA is satisfied by either system S1 or S2
fB
fC
system S1 requires both function fB and fC
S1
S2
S1
Notes: A system may satisfy functions, e.g., a radar may provide the function track airborne target. As it was the case with the functions being satisfied by other functions, this statement allows for an OR aggregation, e.g., this function can be satisfied by this system OR this other system.
A system may require a series of functions, e.g., an SM-2 may require a function called <Launch SM-2> and <Control SM-2>. As it was the case with a function requiring a series of functions, these statements allow for an AND aggregation of the functional requirements, e.g., in order for this system to be operational, this function AND this other function must be achieved.

## Slide 9: Relation Relationships
fA
system S1 requires function fD when performing function fA
fB
fE
system S1 performing function fB is incompatible with system S2 performing function fE
S1
fD
S2
S2
Notes: A system performing a function may require a series of functions, e.g., a SAM with a semi-active seeker will require illumination in order to engage a target. The system may be able to perform other functions, but may be incapable of achieving a sub-set of possible functions if other functions are not achieved. This statement allows for an AND aggregation, e.g., in order for this system to perform the given function, this different function AND this other function must be achieved.
A system performing a function may be incompatible with another system performing a function, e.g., a radar interfering with a satellite communication system, as reported[Brown, 1987] in the case of HMS Sheffield. The radar was not able to search for airborne threats while the SATCOM system was in use, at the same time, the SATCOM system could not receive data while the radar was emitting.

## Slide 10: Disallowed Relationships
These are critical anti-patterns that should not be allowed, along with the associated suggested allowed approach to capture the given relationship

## Slide 11
Q: WHAT IF function fA requires both system S1 and system S2?
A: Each system must be performing a different function that is required by fA
fA,1
S1
S2
fA
fA,2
fA
S1
S2
Q: What is the value of this?
A: It more accurately models reality and can help identify other solutions, e.g., help the user to think of a system S3 that also can satisfy fA,1
Notes: Functions may not require systems, e.g., shooting down an airborne target may not require an SM-2, nor may it require a missile, as this relationship would prescribe a system solution to a particular need. When users specify these relationships they are biasing the solution space. It is possible that the solution the user has in mind is in fact the most effective one, but the system should not allow that relationship to occur because conditions may change, or the user may not have a complete understanding of the possible means to achieve that function. Furthermore, if one was to face the need to state that one function requires more than one system, it is more valuable to decompose that function into the sub-functions the systems in question would perform towards the satisfaction of the former function. This is a better representation of reality because if both systems are required it means that they are inherently performing different functions, each of which is required to satisfy the first function.
What if a function requires two systems? A function is not be allowed to require a system, which must be represented as a function requiring two functions, each of which can be satisfied by one system.

## Slide 12
Q: WHAT IF a system requires another system?
A: A system requires a function which can be performed by a system
S1
S2
fA
S1
S2
Q: What is the value of this?
A: Allows for other systems to also support the function required by S2 and it more explicitly defines what is the relationship between S2 and S1
Notes: Systems may not require another system, e.g., an SM-2 may not require a MK 41 Vertical Launch System (VLS). If a user desires to specify a system requiring another, that system requirement is an indication that the requiring system (e.g., the SM-2 in the prior example) requires a function that is provided by the required system (e.g., the MK 41 VLS may provide “host and launch Standard Missile”). It may be true that at the time of the specification, only one system could provide this functionality, but that does not mandate that another system in the future may not be able to provide the required functionality. By having systems require functions, the framework is made more robust to future developments and can identify functions that may be of interest for future development in order to develop more robust architectures.

## Slide 13
Q: WHAT IF a function is incompatible with another function?
A: A system performing a function may be incompatible with another system performing a function
Q: What is the value of this?
A: Allows future systems to not have this artificial incompatibility
fA
fA
fB
fE
S1
S2
Notes: Functions may not be incompatible with another function, e.g., <detect airborne targets> and <communicate with high throughput over-the-horizon> cannot be made incompatible because their incompatibility arises from the technologies used. During the Falklands War it may have been a true statement that those two functions were incompatible, but as technology progressed, said incompatibilities were removed by using newer systems that did not interfere with one another.

## Slide 14
Q: WHAT IF I have to add a system if two or more systems are selected?
A: This tends to be an artifact of having a system require a function that some systems provide by default, better to make that required function explicit
fA
S1
S3
fC
fB
S1
S2
Q: What is the value of this?
A: It more accurately models reality and can help identify other solutions, e.g., help the user to think of a system S3 that also can satisfy fA,1
S3

## Slide 15
This is an example of an “Add-If” relationship, where a Radio Mount must be included if a particular vehicle hull is selected for a type of radio, but the other hull does not require a special radio mount because it can provide the function directly.
An incompatibility relationship can be specified between functions, but is not required.
Radio Mount
H2-R1
Securely Mount Large Radios
Radio 1
Communicate over UHF
Vehicle Hull 1
Vehicle Hull 2
Structurally Support Vehicle Equipment

## Slide 16: Challenges
Avoid excessive number of functions